1. Functional Requirements
  1. shall continuously monitor the power used from either a 2-phase or a 3-phase installation.
  2. Shall store power usage data locally to be transmitted back to the base station at regular intervals.
  3. Shall display power usage data on an LCD display module integrated into the electric panel.
  4. shall interface and control the digital breakers, monitoring their status and reading the power used on each interface at intervals specified during the setup and install.
  5. Shall be capable of establishing a wireless link with a PICA base station.
  6. Shall be capable of detecting a brownout condition and safely shut itself down.
  7. Shall be capable of restoring its last state after a brownout condition.
  8. Shall be capable of detecting any tampering and alerting both the power-company and the consumer.
  9. Shall integrate with the digital breakers via an SPI bus.
2. Behavioral Requirements
  1. In the event of wireless link loss, attempt to re-establish the wireless link.
  2. In the event of a wireless link loss, revert to stand-alone mode, storing as much data as possible until internal storage is full, then ejecting the oldest data first.
  3. In the event of a wireless link loss, notify the user via the LCD display.
  4. Shall be capable of being configured and upgraded through the base station.
  5. Shall be capable of being configured and upgraded through a local USB port.
  6. Shall perform a built-in-self-test upon system bootup.
  7. In the event of a brownout, the system will dump all of its volatile information to non-volatile storage space.
  8. Shall be able to detect corrupted data when brought out of a brownout condition.
  9. Shall log all events processed in the following 4 categories: critical, error, warning, note.
  10. Store all system critical settings and configuration data in a specified non-volatile storage area.
  11. Shall provide the capability to recover from a bad software update/flash.
3. Software Requirements
  1. shall fit inside of the onboard EEPROM for boot.
  2. Shall perform a system verification on bootup
  3. shall periodically perform a system check to verify the health and status of the system.
  4. Shall store all system critical configuration settings in non-volatile storage.
  5. Shall be user-updateable.
  6. Shall be able to properly recover from a “bad” or “corrupted” software update.
  7. Shall implement a system for authorized access to various components of the system configuration or data display.
4. Hardware Requirements
  1. shall be completely enclosed in a weatherproof case, tolerant of extreme temperature differences.
  2. Shall be completely AC coupled to prevent any transient AC voltages from entering the system.
  3. Shall be grounded in accordance with electrical codes.
  4. Shall comply with all mandated electrical codes for power meters and electrical panels.
  5. Shall be mounted inside the electrical panel in the same location as a standard power meter.
  6. Shall provide non-volatile storage.
5. User Interface Requirements
  1. shall have a 16x4 LCD display module viewable from outside the electric panel.
  2. Shall be capable of interfacing with a simply web-based application for stand-alone configuration.
6. Safety Requirements
  1. shall meet or exceed safety requirements for devices inside an electric panel.
  2. Shall be AC-coupled against incoming line-voltage and current.
  3. Shall be grounded.
  4. Shall be sealed against the elements.
7. Electrical Code Requirements
8. Power Requirements
  1. Shall be capable of operating off of a single breaker tap that provides power to the whole smart-meter system.